## Slide 1: Measurement Principles Recap
If you cannot measure it, then it is not science. —Lord Kelvin
An experiment is a question which science poses to Nature, and a measurement is the recording of Nature's answer. — Max Planck

## Slide 2: Measurement Accuracy versus Precision
Accuracy: refers to how closely measurement agrees with the “true” value
Precision : refers to the resolution with which a measurement is made. For multiple measurements, it can refer to the scatter in the values.
Measurement Error or Uncertainty:
No measurement is exact! All measurements have some inherent error or uncertainty.
Accurate &
precise
Accurate,
Not precise
Precise but,
Not accurate
Not accurate,
Not precise

## Slide 3: Measurement uncertainty and Significant digits
Record all certain digits in a measurement plus last estimated or uncertain digit
Example 1: A length of 10.2 ± 0.1 cm
-state measurement error (uncertainty)
- the uncertainty should match the
measurement precision
Example 2: A mass of 15.05 g ± 0.02 g
All of the digits in these measurements are significant!

## Slide 4
Significant Digits:
All digits in a measured number are significant EXCEPT:
●leading zeros for decimal numbers (as they are placeholders)
●trailing zeros for whole numbers (as they are placeholders)
Counted Values are considered EXACT (infinite significant digits)
Examples:
16.05 kg : ________________
0.0255 s : ________________
170 m : ________________
60.000 mL : ________________
30 students: ________________
1.0025 g: ________________
4 sd
3 sd
2 sd
5 sd
Infinite! (A count)
5 sd

## Slide 5: Weakest Link Rules:
When multiplying/dividing numbers keep the LOWEST number of Significant Digits
Eg. 2.4 cm x 1.563 cm = 3.7512 cm2
3.8 cm2 to 2 sig digs
When adding/subtracting numbers keep the LOWEST number of decimal places
Eg. 1.25 m + 3.865 m + 12 m= 17.115 m
17 m to 0 dp
Should be rounded to:
Should be rounded to:

## Slide 6: New Concept: Absolute and Relative Uncertainty
Absolute error is expressed in the units as the measurement
E.g. 16.5 cm ± 0.2 cm
1.265 kg ± 0.0005 kg
Relative or Percent error is expressed as a percentage of the given measurement
E.g. 3.8 kg ± 2.0 %
5.6 m ± 5.0 %

## Slide 7: Converting between Absolute and Relative Uncertainty
Convert to relative uncertainty:
8.4 kg ± 0.5 kg
Convert to absolute uncertainty:
12.6 m ± 4%
Answer: 8.4 kg ± 6%
Answer: 12.6 ± .5 m

## Slide 8: Propagating Errors
When adding or subtracting numbers we ADD the absolute uncertainties
When multiplying or dividing numbers subtracting numbers we ADD the relative uncertainties
Find the absolute uncertainty when these lengths are added:
(1.5 m ± 0.2 m) + (1.36 m ± 0.05 m) + (2.85 m ± 0.08 m)
=
5.71 m ± 0.33 m  5.7 ± 0.3 m
Find the relative uncertainty when lengths are multiplied to find volume:
(1.5 m ± 0.1 m) x (1.36 m ± 0.05 m) x (2.85 m ± 0.05 m)
=
5.814 m3 ± (6.67% +3.67% + 1.75%)
 5.814 m3 ± 12.1%  5.8 ± 0.7 m3